SUBNETTING

PC1> ip 10.73.0.1/18 10.73.63.254

PC2> ip 10.73.0.2/18 10.73.63.254

PC3> ip 10.73.0.3/18 10.73.63.254

PC4 : 10.73.64.1 255.255.224.0 gateway 10.73.95.254

PC5 : 10.73.64.2 255.255.224.0 gateway 10.73.64.254

PC6 : 10.73.64.3 255.255.224.0 gateway 10.73.64.254

PC7 : 10.73.96.1 255.255.248.0 gateway 10.73.96.254

PC8 : 10.73.96.2 255.255.248.0 gateway 10.73.96.254

PC9 : 10.73.96.3 255.255.248.0 gateway 10.73.96.254

LACP

SW1, SW2, SW3:
interface GigabitEthernet 0/0
channel-group 1 mode active
interface GigabitEthernet 0/2
channel-group 1 mode active
interface GigabitEthernet 0/1
channel-group 2 mode active
interface GigabitEthernet 0/3
channel-group 2 mode active

SW-R1, SW-R2:
interface GigabitEthernet 0/0
channel-group 1 mode active
interface GigabitEthernet 2/0
channel-group 1 mode active
interface GigabitEthernet 0/1
channel-group 2 mode active
interface GigabitEthernet 2/1
channel-group 2 mode active
interface GigabitEthernet 0/2
channel-group 3 mode active
interface GigabitEthernet 2/2
channel-group 3 mode active

EN SW-R1 y en SW-R2:

interface range GigabitEthernet 0/0-2
switchport trunk encapsulation dot1q
switchport trunk allowed vlan 10,20,30
end
interface range GigabitEthernet 2/0-2
switchport trunk encapsulation dot1q
switchport trunk allowed vlan 10,20,30
end

EN SW1, SW2 y SW3:

interface range gigabitEthernet 0/0-3
switchport trunk encapsulation dot1q
switchport trunk allowed vlan 10,20,30

Ahora haré VRRP en los SW de capa nucleo:

En SW-R1:

SW-R1(config)#interface vlan 10
SW-R1(config-if)#ip address 10.73.0.253 255.255.192.0
no shut	down
SW-R1(config-if)#vrrp 10 ip 10.73.0.254
SW-R1(config-if)#vrrp 10 priority 1
end
SW-R1(config)#interface vlan 20
SW-R1(config-if)#ip address 10.73.64.253 255.255.224.0
no shut	down
SW-R1(config-if)#vrrp 20 ip 10.73.64.254
SW-R1(config-if)#vrrp 20 priority 1
end

SW-R1(config)#interface vlan 30
SW-R1(config-if)#ip address 10.73.96.253 255.255.248.0
no shut	down
SW-R1(config-if)#vrrp 30 ip 10.73.96.254
SW-R1(config-if)#vrrp 30 priority 1
end

Lo mismo en SW-R2(1 valor menos de ip):

SW-R2(config)#interface vlan 10
SW-R2(config-if)#ip address 10.73.0.252 255.255.192.0
no shut	down
SW-R2(config-if)#vrrp 10 ip 10.73.0.254
SW-R2(config-if)#vrrp 10 priority 1
end
SW-R2(config)#interface vlan 20
SW-R2(config-if)#ip address 10.73.64.252 255.255.224.0
no shut	down
SW-R2(config-if)#vrrp 20 ip 10.73.64.254
SW-R2(config-if)#vrrp 20 priority 1
end

SW-R2(config)#interface vlan 30
SW-R2(config-if)#ip address 10.73.96.252 255.255.248.0
no shut	down
SW-R2(config-if)#vrrp 30 ip 10.73.96.254
SW-R2(config-if)#vrrp 30 priority 1
end

En SW1, SW2, SW3:
SW1(config)#interface range gigabitEthernet 1/0-3
SW1(config-if-range)#switchport trunk encapsulation dot1q
SW1(config-if-range)#switchport trunk allowed vlan 10

SW1(config)#interface range gigabitEthernet 2/0-3
SW1(config-if-range)#switchport trunk encapsulation dot1q
SW1(config-if-range)#switchport trunk allowed vlan 20

SW1(config)#interface range gigabitEthernet 3/0-3
SW1(config-if-range)#switchport trunk encapsulation dot1q
SW1(config-if-range)#switchport trunk allowed vlan 30

En ISP1-Principal:

R1(config)#interface gigabitEthernet 0/0
R1(config-if)#ip address 10.73.104.2 255.255.255.252
R1(config-if)#no shutdown

R1(config)#interface gigabitEthernet 0/1
R1(config-if)#ip address 10.73.104.6 255.255.255.252
R1(config-if)#no shutdown

En ISP2-Respaldo:

R2(config)#interface gigabitEthernet 0/0
R2(config-if)#ip address 10.73.104.10 255.255.255.252
R2(config-if)#no shutdown

R(config)#interface gigabitEthernet 0/1
R2(config-if)#ip address 10.73.104.14 255.255.255.252
R2(config-if)#no shutdown

SW-R1(config)#interface gigabitEthernet 1/0
SW-R1(config-if)#no switchport	//Hace que el switch se comporte como router
SW-R1(config-if)#ip address 10.73.104.1 255.255.255.252
SW-R1(config-if)#no shutdown

SW-R1(config)#interface gigabitEthernet 1/1
SW-R1(config-if)#no switchport
SW-R1(config-if)#ip address 10.73.104.9 255.255.255.252
SW-R1(config-if)#no shu
SW-R1(config-if)#no shutdown

SW-R2(config)#interface gigabitEthernet 1/0
SW-R2(config-if)#no switchport
SW-R2(config-if)#ip address 10.73.104.5 255.255.255.252
SW-R2(config-if)#no shutdown

SW-R2(config)#interface gigabitEthernet 1/1
SW-R2(config-if)#no switchport
SW-R2(config-if)#ip address 10.73.104.13 255.255.255.252
SW-R2(config-if)#no shutdown

En SW1, SW2 y SW3:
SW1(config)#interface range gigabitEthernet 1/0-3
SW1(config-if-range)#switchport mode access
SW1(config-if-range)#switchport access vlan 10

SW1(config)#interface range gigabitEthernet 2/0-3
SW1(config-if-range)#switchport mode access
SW1(config-if-range)#switchport access vlan 20

SW1(config)#interface range gigabitEthernet 3/0-3
SW1(config-if-range)#switchport mode access
SW1(config-if-range)#switchport access vlan 30

STP:
SW1(config)#spanning-tree mode rapid-pvst
SW1(config)#interface gigabitEthernet 1/0
SW1(config-if)#spanning-tree portfast
SW1(config)#interface gigabitEthernet 2/0
SW1(config-if)#spanning-tree portfast
SW1(config)#interface gigabitEthernet 3/0
SW1(config-if)#spanning-tree portfast

SW-R1(config)#spanning-tree vlan 10 root primary
SW-R1(config)#spanning-tree vlan 20 root primary
SW-R2(config)#spanning-tree vlan 30 root primary

SW-R1(config)#ip route 0.0.0.0 0.0.0.0 10.73.104.2
SW-R1(config)#ip route 0.0.0.0 0.0.0.0 10.73.104.10 10

SW-R2(config)#ip route 0.0.0.0 0.0.0.0 10.73.104.6
SW-R2(config)#ip route 0.0.0.0 0.0.0.0 10.73.104.14 10

En R1 y R2:
R1(config)#interface loopback 1
R1(config)#ip address 99.99.99.99 255.255.255.255

R1(config)#ip route 10.73.0.0 255.255.192.0 10.73.104.1
R1(config)#ip route 10.73.0.0 255.255.192.0 10.73.104.5 10
R1(config)#ip route 10.73.64.0 255.255.224.0 10.73.104.1
R1(config)#ip route 10.73.64.0 255.255.224.0 10.73.104.5 10
R1(config)#ip route 10.73.96.0 255.255.248.0 10.73.104.1 10
R1(config)#ip route 10.73.96.0 255.255.248.0 10.73.104.5

R2(config)#ip route 10.73.0.0 255.255.192.0 10.73.104.9
R2(config)#ip route 10.73.0.0 255.255.192.0 10.73.104.13 10
R2(config)#ip route 10.73.64.0 255.255.224.0 10.73.104.9
R2(config)#ip route 10.73.64.0 255.255.224.0 10.73.104.13 10
R2(config)#ip route 10.73.96.0 255.255.248.0 10.73.104.13
R2(config)#ip route 10.73.96.0 255.255.248.0 10.73.104.9 10

SACAR MODO TRUNK En las interfaces entre Sw1 y pcs, y demás sw y pcs.

HACER LACP